## Slide 1: The Nanopore Field Effect Transistor (FET) for Protein Analysis
Nanopore technology has revolutionized DNA sequencing, and nascent nanopore-based technology breakthroughs may be anticipated to lead to revolutions in protein analysis.
Present-day nanopore tech relies on the recording of very small (∼pA-nA) ionic currents. Such low currents limit recording bandwidth and impose a translocation speed limit.
Koen Martens1,2, David Barge1,2, Colin Locquart1,2, Sybren Santermans1, Lijun Liu1,2, Jacobus Delport1,2, Bert Du Bois1, Anne Verhulst1,2, Simone Severi1, Pol Van Dorpe1,2
Solid-state nanopore
bioFET
6.5nm
Restrepo-Perez et al.
Nanoscale 2017
Olsen et al.
JACS 2013
Chemically robust (vs. biopore)
SiO2 and/or Si3N4 surfaces
High molecule throughput
In theory up to millions/s
not same as molecules detected
Low ion current (pA-nA), low bandwidth(1kHz-1MHz), cannot sense quickly translocating molecules
Difficult to integrate on chip
High spatial resolution toward sequencing (vs. biopore) undemonstrated
Chemically robust
SiO2 and/or Si3N4 surfaces
Low molecule throughput
surface capture/docking, enzymatic
High FET current, high bandwidth, sense very fast changes
A currents, 1-100MHz bandwidth or more
Can be massively integrated on chip
up to billions per chip
Spatial resolution (e.g. linked to enzyme) undemonstrated
DNA polymerase I
Klenow Fragment
Translocating molecule modulates the recorded ionic current passing through pore
Molecule docks close (1-10nm) to FET surface. Molecule’s charge modulates channel charge and FET current
Chemically robust (vs. biopore)
High molecule throughput
As in nanopore
High FET current, high bandwidth
senses both resistive divider effect and/or charge
Can be massively integrated on chip
Millions to billions per chip
High spatial resolution undemonstrated
Nanopore FET
The best-of-both-worlds combination of nanopores and bioFETs:
Imec’s nanopores, bioFETs and nanopore FETs
A nanopore wrapped by a nanoscale field-effect transistor (FET). The FET senses single molecules translocating through the pore
The NPFET promises:
higher bandwidths, breaking of nanopore speed limit
easy integration into large arrays
 orders of magnitude greater molecular sensing throughput
+
=
Nanopore
BioFET
Nanopore FET
Mass-manufacturable, lithographically patterned 25nm diameter nanopores with low capacitance membranes for increased bandwidth and signal-to-noise ratio
TEM
cross-section
of nanopore
Schematic cross-section of membrane and pore
Thick 0.75um oxide
For low capacitance
bioFET
TEM cross-section
Clear signal of ~ 17 mV for 500 nM DNA = 8x1011 DNA/cm-2 (TXRF)
~ 37 molecules for smallest measured device: (13+2×19)×90 nm2
Sub-70 nm long FETs show potential for single-molecule detection
1.5 mM PBS: SNR > 5
Santermans et al.
IEDM 2020
Modeled (TCAD) single-molecule outlook
World’s smallest bioFETs
down to 50 nm gate length
milestone of fabrication and characterization of the NPFET.
lithography based nanopore formation and opening in the nanowire channel is realized, with nanopore diameter down to 20-30 nm, silicon channel as thin as 4 nm.
The NPFET has excellent electrical characteristics
Top view SEM
Modeling work with dedicated nanoelectronics-nanofluidics simulator: Major sensitivity boost obtained when biasing NPFET in the exponentially sensitive subthreshold regime
Verhulst et al. IEEE Sensors 2022
Single molecule proteomics-on-chip massively parallel system vision
...
Protein/biopolymer sample
101100110
protein identity
sensor device
103-106 devices/chip
103-106 molecules/s
Proteomics-on-chip demands single-molecule
Achilles heel of single-molecule fluorescence methods: limited throughput, difficulties to improve dynamic range vs. MS
Sense freely translocating molecules at high bandwidth  high throughput, potential dynamic range 108-1012 vs. MS 105